Selecting the appropriate Resultant Flood Zone

If the subject elevation is below the BFE…

Select the Flood Zone that the subject property is shown in on the effective FIRM.

If the subject elevation is above the BFE…

The subject should be removed to Zone X (unshaded) or Zone C if the Lowest Adjacent Grade (LAG) or Lowest Lot Elevation (LLE) is above the 1% Annual Chance Flood (100-Year Flood or BFE) elevation and above the 0.2% Annual Chance Flood (500-Year Flood) elevation, or if the subject elevation is above the 1% Annual Chance Flood (BFE) elevation and there is no 0.2% Annual Chance Flood elevation listed in the FIS report.

The subject should be removed to Zone X (shaded) or Zone B when the Lowest Adjacent Grade (LAG) or Lowest Lot Elevation (LLE) is above the 1% Annual Chance Flood (100-Year Flood or BFE) elevation but below the 0.2% Annual Chance Flood (500-Year Flood) elevation or when the Lowest Adjacent Grade (LAG) or Lowest Lot Elevation (LLE) is equal to the 1% Annual Chance Flood (100-Year Flood or BFE).